## Slide 1: Matrix: Multihop Address Allocation and Dynamic Any-to-Any Routing for 6LoWPAN
Bruna S. Peres Otavio A. O. Souza Bruno P. Santos Edson R. A. Junior
Olga Goussevskaia Marcos A. M. Vieira Luiz F. M. Vieira Antônio A. F. Loureiro
MSWiM 2016
Malta, November 16th, 2016

## Slide 2: 6LoWPAN
IPv6 over Low-power Wireless Personal Area Networks
Even the smallest low-power devices should be able to run the Internet Protocol to become part of the Internet of Things

## Slide 3: Problem
Unstructured addresses that do not reflect the topology of the network
Routing lacks support for any-to-any communication or do not perform it in a efficient manner
Internet
LBR-1
A
C
H
G
W
X
E
K
T
L
F
J
D
B

## Slide 4: Motivation
Reliable any-to-any communication
Message and memory-efficient
New applications for the Internet of Things

## Slide 5: Collection Tree Protocol - CTP
Collection tree
Does not support top-down data traffic
No top-down data traffic!

## Slide 6: RPL - IPv6 Routing Protocol for Low-Power and Lossy Networks
Distance vector routing protocol specifically designed for 6LoWPAN
Builds and maintains an acyclic network topology, directed at the root (DAG)
Defines two modes of operation for top-down data flows

## Slide 7: Non-storing mode
To: D
C-G-D
C
B
E
H
G
F
I
A
D
Dst | Nxt-hop
A | C – G - A
B | B
C | C
D | C – G - D
E | E
F | B - F
G | C - G
H | C - H
I | E - I
To: D
LBR-1
Longer paths!
Root becomes a bottleneck!

## Slide 8: Storing-mode
LBR-1
C
B
E
H
G
F
I
A
D
Dst | Nxt-hop
A | G
D | G
G | G
H | H
Dst | Nxt-hop
A | C
B | B
C | C
D | C
E | E
F | B
G | C
H | C
I | E
To: D
Dst | Nxt-hop
A | A
D | D
Extensive routing tables!
O(n)

## Slide 9: Matrix
Hierarchical IPv6 address optimizing routing table size
Local broadcast mechanism to forward messages when persistent node or link failures occur
Internet
::0000 to ::A7C0
::5427 to ::A7C0
::580F to ::A7C0
::5810 to :: 8001
::83EA to ::A7C0
:: 8002 to ::A7C0
::0001 to ::2D17
::2D18 to ::5426
::0020 to ::2D17
::0078 to ::2D17
::2D62 to ::486E
::486F to ::5426
::4C6B to ::5426
::2E4C to ::3539
::353A to ::486E

## Slide 10: Matrix
Multihop Address Allocation and Dynamic Any-to-Any Routing for 6LoWPAN
Underlying collection tree topology:
  Nodes have static location
  Links are dynamic

## Slide 11: Matrix
Three simultaneous distributed trees:
  Collection tree (Ctree)
  IPv6 address tree (IPtree)
  Reverse collection tree (RCtree)
1
2
3
4
5
6
7
8

## Slide 12: Matrix
Three simultaneous distributed trees:
  Collection tree (Ctree)
  IPv6 address tree (IPtree)
  Reverse collection tree (RCtree)
0
199A
2084
3F9E
7D5D
5EB8
6ED9
977D

## Slide 13: Matrix
Three simultaneous distributed trees:
  Collection tree (Ctree)
  IPv6 address tree (IPtree)
  Reverse collection tree (RCtree)
0
199A
2084
5EB8
977D
6ED9
7D5D
3F9E
1
2
3
4
5
6
7
8
Ctree
RCtree

## Slide 14: Matrix
Alternative routing tree:
0
199A
2084
5EB8
977D
6ED9
7D5D
3F9E

## Slide 15: IPv6 Multihop Host Configuration
Collection tree initialization

## Slide 16: IPv6 Multihop Host Configuration
1
1
1
1
1
3
5
2
2
Descendants convergecast

## Slide 17: IPv6 Multihop Host Configuration
A-L
M-P
Q-V
A-B
C-H
M-N
Q-T
C-D
E-F
Z
L
P
V
B
H
N
T
D
F
A-Z
Address partitioning procedure
X-Y
saves
For delayed connections

## Slide 18: IPv6 Multihop Host Configuration
A-Z
L
P
V
B
H
N
T
D
F
A-L
A-B
C-H
C-D
E-F
M-P
M-N
Q-V
Q-T
Z
INIT | FINAL
A | L
M | P
Q | V
NEXT HOP
INIT | FINAL
A | B
C | H
RANGE
L
To: D
O(k)
Standard routing

## Slide 19: What if....
L
P
V
B
H
N
T
D
F
A-L
A-B
C-H
C-D
E-F
M-P
M-N
Q-V
Q-T
Z
A-Z

## Slide 20: Local Broadcast
Z
V
L
H
D
IParent(H)
CTparent(H)
To: D
T1
T2
Fault tolerance and network dynamics
Alternative top-down routing

## Slide 21: Local Broadcast
Z
V
L
H
D
IParent(H)
CTparent(H)
To: D
T1
T2
Fault tolerance and network dynamics
Alternative top-down routing

## Slide 22: Local Broadcast
INIT | FINAL
T1.init | T2.final
T2.init | T2.final
INIT | FINAL
D | H
Z
V
L
H
D
IParent(H)
CTparent(H)
CTparent(H)
T1
T2
To: D
To: D
To: D
To: D
To: D
To: D
Fault tolerance and network dynamics
Alternative top-down routing

## Slide 23: Local Broadcast
Z
V
L
H
D
IParent(H)
CTparent(H)
To: D
T1
T2
Fault tolerance and network dynamics
Alternative top-down routing

## Slide 24: Evaluation
Matrix was implemented as a subroutine of CTP in TinyOS and the experiments were run using the TOSSIM
We compare Matrix with RPL*, MHCL and CTP
We use the LinkLayerModel tool from TinyOS to generate the topology and connectivity model
*RPL was implemented in Contiki and simulated on Cooja

## Slide 25: Simulation parameters
Parameter | Value
Base Station | 1 center
Number of Nodes | 100
Radio Range (m) | 100
Density (nodes/m²) | 10
Number of experiments | 10
Path Loss Exponent | 4.7
Power decay (dB) | 55.4
Shadowing Std Dev (dB) | 3.2
Simulation duration | 20 min
Application messages (node to root + ack) | 10 per node
Max. Routing table size | 20 entries

## Slide 26: Faulty network scenarios
σ/ε | 10 sec. | 20 sec. | 40 sec.
1% | Scenario 2 | Scenario 3 | Scenario 4
5% | Scenario 5 | Scenario 6 | Scenario 7
10% | Scenario 8 | Scenario 9 | Scenario 10
After every 60 seconds of simulation, each node shutdowns its radio with probability σ and keeps the radio off for a time interval uniformly distributed in [ε-5, ε+5] seconds
5% chance to keep the radio off for [15,25] seconds

## Slide 27: Routing table usage CDF
> 35% of nodes are leaves
30%
RPL is the only protocol that uses 100% of table entries

## Slide 28: Number of control packets
MSiM 2016
Malta, November 16th
2x more
More failures

## Slide 29: Top-down routing success rate
20%
number of messages lost due to a failure of the destination node
More failures

## Slide 30: Top-down routing success rate
More failures
2/3 of otherwise lost messages succeed in reaching the final destination
number of messages lost due to a failure of the destination node

## Slide 31: Matrix: Multihop Address Allocation and Dynamic Any-to-Any Routing for 6LoWPAN
Network initialization
Reliable any-to-any communication
::83EA to ::A7C0
:: 8002 to ::A7C0
::580F to ::A7C0
::5810 to :: 8001
::0000 to ::A7C0
Internet
::5427 to ::A7C0

## Slide 32: Future direction
Experimentation

## Slide 33: Future direction
Experimentation
Mobility
::83EA to ::A7C0
:: 8002 to ::A7C0
::580F to ::A7C0
::5810 to :: 8001
::0000 to ::A7C0
Internet
::5427 to ::A7C0

## Slide 34: Matrix: Multihop Address Allocation and Dynamic Any-to-Any Routing for 6LoWPAN
Bruna S. Peres Otavio A. O. Souza Bruno P. Santos Edson R. A. Junior
Olga Goussevskaia Marcos A. M. Vieira Luiz F. M. Vieira Antônio A. F. Loureiro